## Slide 1: NAME: KORIR KIBET JOVAN. REG NO : EO24-01-2289/2020. BSC. CIVIL ENGINEERING.
UNIT: CRITICAL THINKING AND COMMUNICATION SKILLS.
UNIT CODE: IGS 4101
TASK: SOIL STABILIZATION POWERPOINT PRESENTATION

## Slide 2: INTRODUCTION
Soil stabilization is the process of improving soil properties more so the engineering properties by, implementing chemical and mechanical techniques.
Mainly aimed at increasing the shear strength and shrink-swell property of a soil, hence the subgrade bearing capacity is increased to the desired levels. Soil stabilization is used to reduce permeability and compressibility of the soil mass in earth structures and to increase its shear strength.

## Slide 3: CONT…
Done when problematic soil is a subgrade with low bearing capacity. Problematic soils, from a geotechnical point of view, are soils that have the potential to expand, collapse, disperse, undergo excessive settlement or even fail under relatively low stress conditions.
Stabilization can be done mechanically or chemically. Mechanically the problematic soil are mixed with well graded soil meeting desired engineering properties hence improving their gradation.

## Slide 4: CONT…
Chemically, additives are used to improve the texture, increase strength and reduce swell characteristics, maintain soil moisture content, increase soil particle cohesion and serve as cementing and water proofing agents.
Stabilizing additives vary from construction wastes to chemical materials produced from factories and include: lime, cement, chemicals, fly ash, Rice Husk, ash and bituminous Stabilization agents.
The impact of this additives is determined by the amount of additive used and the soil type being stabilized.
The soil must be able to react with the chemical additives to achieve the soil desired improvement.

## Slide 5: BODY
Factors taken into consideration when choosing a stabilization technique include;
Designing the soil mix with stability and durability values.
Considering the construction procedure by adequately compacting the stabilized layers.

## Slide 6: CONT…
Evaluating the properties of the given type of soil- .This determines soils’ engineering properties a given soil possess.
Deciding the most suitable, effective and economical method of soil stabilization for supplementing the lacking properties.
Soil stabilization method vary with soil type according to properties. Even if possible, it may not be economically suitable. Hence stabilization method should be prudently chosen.

## Slide 7: MECHANICAL STABILIZATION
Involves changing of soil’s gradation. Two or more types of natural soils are mixed to obtain a composite mixture with superior soil properties.
For the composite soil to achieve the desired gradation, coarse soils are added or some fine soils are removed.
Soils are divided into two; aggregates which are soils with granular bearing skeleton and have particles of size retained by sieve No. 200 and, binders which as the soils passing through sieve No. 200 and do not possess a bearing skeleton.

## Slide 8: CONT…
Proper blending of aggregates and binders is done to achieve the required gradation. The blended soil should possess both internal friction and cohesion.
This process includes soil compaction and densification by application of mechanical energy using various sorts of rollers, rammers, vibration techniques and sometime blasting.
The stability of the soil in this method relies on the inherent properties of the soil material.

## Slide 9: CHEMICAL STABILIZATION
Admixtures used as soil stabilizers includes the following;
Chemical stabilization involves stabilizing soils by use of different chemicals. In chemical stabilization, curing time and setting time can be controlled. Chemicals used in stabilization; Calcium and Sodium chloride and Sodium silicate.
Thermal stabilization of soils is done either by heating (water content decreases reducing electrical repulsion, increasing soil strength) or cooling (temperature is reduced to the freezing point, the pore water freezes and the soil becomes stabilized) of soils.

## Slide 10: CONT…
Stabilization by grouting-It is a method of soil stabilization in which stabilizers are injected into the soil under pressure. The stabilizers have high viscosity and is suitable for stabilizing highly permeable soils.
Bituminous stabilization-used for inorganic soil which can be mixed with asphalt. In cohesionless soils, asphalt acts as a binding agent by bonding soil particles together.

## Slide 11: CONT…
In cohesive soils, asphalt protects the soil by plugging its voids and water proofing. Cohesive soils can therefore maintain low moisture content as water since infiltration is checked. The result is increase in the soil bearing capacity. The amount of bitumen used for stabilization ranges from 4% to 7% by weight.
Lime stabilization-use of quick lime or hydrated lime, and is suited for use on fine grained soils with a little clay having raised level of silica in it.

## Slide 12: CONT…
Through optimum moisture content, strength and shrinkage limit are raised while liquid limit, maximum density and plasticity index is lowered. Lowering of plastic index is attained by increase in plastic limit and lowering of liquid limit.
Fly Ash stabilization-Fly ash, a waste product of coal production has pozzolans that initiate chemical reactions that increase the strength of soils for geotechnical applications. Increase slightly yield strength but better flowability, lower plastic viscosity and much higher chloride resistance.

## Slide 13: CONT…
Rice husk stabilization-RHA IS Locally available from rice milling factories. To obtain optimum stabilization effect the content of rice husk ash should be 20%-30% depending on soil. RHA is a pozzolana with around 90% silica and relatively 2% of each aluminum and iron oxides. The three components are responsible for pozzolanic reactions.

## Slide 14: CONT…
Cement Stabilization- soil particles bonding is caused by hydration of the cement particles which grow into crystals that interlock with one another giving a high compressive strength. Cement helps reduce soils’ liquid limit and plasticity index as well as workability of clay soils. Cement used include; Ordinary Portland cement, Blast furnace cement, Sulfate resistant cement and High alumina cement.

## Slide 15: ADVANTAGES OF SOIL STABILIZATION
Saves time; reduces the time required for construction projects by improving soil quality and workability of soils such as cohesive clays.
Waste utilization; Stabilization techniques incorporate waste materials such as fly ash, lime or cement utilizing them into useful resources and reducing the need for landfill spaces.

## Slide 16: CONT…
Economic advantage; The long-term cost of soil stabilization is saved over the lifecycle of the project because by improving soil quality, the need for additional materials for replacement of problematic soils, equipment and maintenance cost is minimized.
Technical advantage; Stabilized soils can be used for a wide range of construction projects

## Slide 17: CONT…
Environmental conservation; Soil stabilization helps preserve environment by reducing soil erosion, dust generation and, consumption of natural resources. It also promotes utilization of recycled products and minimization of waste generation.
All season working; Stabilized soils are less susceptible to weather-related disruptions, allowing construction activities to continue even during winter months when traditional methods might be impractical due to freezing temperatures or moistures.

## Slide 18: CONT…
Savings by design; Properly stabilized soils can reduce the need for extensive structural designs and reinforcements, resulting in cost savings during planning and construction phases